## Slide 1: Mechanical Ventilation Management
Comprehensive Guide to Ventilator Management
Presenter: [Name], RRT
Date: [Date]
Department: Respiratory Care

## Slide 2: Learning Objectives
By the end of this session, participants will be able to:
  Describe the components of a mechanical ventilator and breathing circuit
  Select appropriate ventilator modes based on patient condition
  Apply lung-protective ventilation strategies
  Interpret ventilator graphics and waveforms
  Troubleshoot common ventilator alarms and patient-ventilator asynchrony
  Develop and implement ventilator weaning protocols
Notes: Mechanical ventilation is a core skill for respiratory therapists. This presentation covers essential concepts.

## Slide 3: Indications for Mechanical Ventilation
Primary Indications:
Apnea or Respiratory Arrest
  No spontaneous breathing
  Immediate intervention required
Acute Respiratory Failure
  Hypoxemic: PaO2 <60 mmHg on high FIO2
  Hypercapnic: pH <7.30 with elevated PaCO2
  Increased work of breathing
Airway Protection
  Altered mental status (GCS ≤8)
  Inability to protect airway
  Risk of aspiration
Prophylactic/Perioperative
  Major surgery
  Hemodynamic instability
  Severe metabolic acidosis
Notes: Indications for mechanical ventilation include respiratory failure, airway protection, and perioperative support.

## Slide 4: Ventilator Components
The Mechanical Ventilator System
Control System:
  Microprocessor control
  User interface
  Monitoring displays
  Alarm systems
Pneumatic System:
  Gas source (wall oxygen, medical air)
  Pressure regulators
  Flow controllers
  Valves
Breathing Circuit:
  Inspiratory limb
  Expiratory limb
  Y-connector
  Humidifier
  HME or heated humidifier
Patient Interface:
  Endotracheal tube
  Tracheostomy tube
  Mask (for NIV)
Notes: Understanding ventilator components is essential for troubleshooting and proper setup.

## Slide 5: Ventilator Modes: Overview
Classification by Control Variable
Volume Control (VC)
  Delivers set tidal volume
  Pressure varies with compliance/resistance
  Guaranteed minute ventilation
  Examples: VC-AC, VC-SIMV
Pressure Control (PC)
  Delivers set inspiratory pressure
  Volume varies with compliance/resistance
  Decelerating flow pattern
  Examples: PC-AC, PC-SIMV, PRVC
Pressure Support (PS)
  Patient-triggered, pressure-limited
  Flow-cycled
  Used for spontaneous breathing
Notes: Ventilator modes are classified by what variable is controlled: volume, pressure, or support.

## Slide 6: Ventilator Modes: Assist/Control (A/C)
Volume Assist/Control
Characteristics:
  All breaths are volume-controlled
  Patient can trigger breaths
  If no trigger, ventilator delivers at set rate
  Every breath has same volume
Settings:
  Tidal volume (VT)
  Respiratory rate (RR)
  FIO2
  PEEP
  Flow rate
  Inspiratory time or I:E ratio
Advantages:
  Guaranteed minute ventilation
  Good for patients with no spontaneous effort
Disadvantages:
  Can cause asynchrony if patient wants different pattern
  Risk of barotrauma if patient fights ventilator
Notes: A/C mode ensures every breath delivers the set volume. It's commonly used for patients requiring full support.

## Slide 7: Ventilator Modes: SIMV
Synchronized Intermittent Mandatory Ventilation
Characteristics:
  Set number of mandatory breaths (volume or pressure)
  Patient can breathe spontaneously between mandatory breaths
  Spontaneous breaths can be unsupported or pressure-supported
Settings:
  Mandatory rate
  Tidal volume (if VC) or pressure (if PC)
  Pressure support for spontaneous breaths
  FIO2, PEEP
Advantages:
  Allows spontaneous breathing
  May reduce sedation needs
  Theoretically prevents respiratory muscle atrophy
Disadvantages:
  Can increase work of breathing
  May prolong weaning
  Not proven superior to A/C
Notes: SIMV allows spontaneous breathing between mandatory breaths. Its benefits over A/C are not well established.

## Slide 8: Ventilator Modes: Pressure Support
Spontaneous Mode with Support
Characteristics:
  Patient triggers every breath
  Set pressure support level
  Flow-cycled (cycles off when flow drops to % of peak)
  No set rate or tidal volume
Settings:
  Pressure support level (cmH2O)
  PEEP
  FIO2
  Trigger sensitivity
  Flow cycle criteria
Advantages:
  Patient controls rate and tidal volume
  Comfortable for awake patients
  Good for weaning
Disadvantages:
  No guaranteed minute ventilation
  Apnea alarm essential
  Not for patients with weak drive
Notes: Pressure support is comfortable for patients and commonly used for weaning from mechanical ventilation.

## Slide 9: Ventilator Modes: Advanced Modes
Pressure Regulated Volume Control (PRVC/VC+)
Characteristics:
  Pressure-controlled breaths
  Volume-targeted
  Automatically adjusts pressure to deliver set volume
Advantages:
  Decelerating flow (better distribution)
  Volume guarantee
  Automatic compliance compensation
Airway Pressure Release Ventilation (APRV)
Characteristics:
  Two pressure levels (Phigh and Plow)
  Spontaneous breathing allowed at both levels
  Time-cycled release
Advantages:
  Good oxygenation
  Allows spontaneous breathing
  Lower peak pressures
Notes: Advanced modes combine benefits of pressure and volume control. APRV is useful for refractory hypoxemia.

## Slide 10: Lung-Protective Ventilation
ARDSNet Protocol Principles
Tidal Volume:
  6 ml/kg ideal body weight
  Range: 4-8 ml/kg
  Calculate IBW:
  Men: 50 + 2.3 × (height in inches - 60)
  Women: 45.5 + 2.3 × (height in inches - 60)
Plateau Pressure:
  Goal: <30 cmH2O
  If >30: decrease VT to minimum 4 ml/kg
PEEP:
  Start at 5 cmH2O
  Titrate using PEEP/FIO2 tables
  Balance oxygenation vs. hemodynamics
Permissive Hypercapnia:
  Accept PaCO2 up to 60 if pH ≥7.25
  Don't increase VT to normalize CO2
Notes: Lung-protective ventilation reduces ventilator-induced lung injury. The ARDSNet protocol is the standard of care.

## Slide 11: Initial Ventilator Setup
Standard Starting Points
Volume A/C Mode:
| Parameter | Setting | Notes |
|-----------|---------|-------|
| VT | 6-8 ml/kg IBW | Use IBW, not actual weight |
| Rate | 12-16/min | Adjust for pH/CO2 |
| FIO2 | 100% | Titrate down quickly |
| PEEP | 5 cmH2O | Minimum to prevent atelectasis |
| Flow | 60 L/min | Adequate for most adults |
| I:E ratio | 1:2 to 1:3 | Avoid inverse ratio |
Post-Intubation:
  Check bilateral breath sounds
  Verify ET tube position (depth marking)
  Obtain chest X-ray
  Check ABG in 30 minutes
Notes: Standard initial settings provide a starting point. Always adjust based on patient response and ABG results.

## Slide 12: Ventilator Graphics
Understanding Waveforms
Pressure-Time Waveform:
  Shows pressure changes during breath
  Peak pressure: Total resistance + compliance
  Plateau pressure: Static compliance only
  PEEP: Baseline pressure
Flow-Time Waveform:
  Square wave (constant flow) - volume control
  Decelerating wave - pressure control
  Expiratory flow shows airway obstruction
Volume-Time Waveform:
  Shows volume delivery and exhalation
  Should return to zero
  If not, air trapping present
Notes: Ventilator graphics provide valuable information about patient-ventilator interaction and lung mechanics.

## Slide 13: Ventilator Graphics Interpretation
Common Patterns
Normal:
  Smooth, consistent waveforms
  Volume returns to baseline
  Stable pressures
Airway Obstruction:
  Prolonged expiratory flow
  Scalloped expiratory flow waveform
  Auto-PEEP
Asynchrony:
  Pressure waveform notches (triggering issues)
  Flow waveform abnormalities
  Double triggering
Bronchodilator Response:
  Decreased peak pressure
  Improved expiratory flow
  Reduced auto-PEEP
Notes: Recognizing waveform patterns helps identify patient-ventilator asynchrony and response to treatment.

## Slide 14: Patient-Ventilator Asynchrony
Types and Solutions
Trigger Asynchrony:
  Problem: Patient effort doesn't trigger breath
  Cause: Insensitive trigger, auto-PEEP
  Solution: Increase sensitivity, reduce auto-PEEP
Flow Asynchrony:
  Problem: Set flow doesn't match patient demand
  Cause: Flow too low for patient's needs
  Solution: Increase flow or switch to pressure control
Cycle Asynchrony:
  Problem: Inspiration ends too early or late
  Cause: Mismatch between neural and mechanical inspiration
  Solution: Adjust flow cycle % or inspiratory time
Double Triggering:
  Problem: Two breaths in rapid succession
  Cause: Insufficient tidal volume, short inspiratory time
  Solution: Increase VT or adjust flow
Notes: Asynchrony increases work of breathing and patient discomfort. Identifying the type guides correction.

## Slide 15: Ventilator Alarms: High Pressure
Causes:
  Secretions in airway
  Kinked ETT or circuit
  Bronchospasm
  Decreased lung compliance
  Patient biting ETT
  Water in circuit
  Coughing or fighting ventilator
Response:
  1. Check patient first - look, listen, feel
  2. Suction if indicated
  3. Check circuit for kinks or water
4. Auscultate for bronchospasm
5. Check ETT position and patency
6. Consider sedation if patient-ventilator dyssynchrony
7. If unresolved, disconnect and bag manually
Notes: Always check the patient first when alarms sound. Systematic troubleshooting resolves most issues.

## Slide 16: Ventilator Alarms: Low Pressure/Volume
Causes:
  Circuit disconnect
  Cuff leak
  Patient self-extubation
  Leak in circuit
Response:
  1. Check patient immediately
  2. Verify ETT position (depth marking)
  3. Check cuff pressure (20-30 cmH2O)
4. Check all connections
5. Listen for leak around ETT
6. If extubated, bag-valve-mask and call for help
Low PEEP/CPAP Alarm:
  Large leak in system
  Circuit disconnect
  Inadequate flow
Notes: Low pressure alarms may indicate a critical disconnection. Respond immediately to check the patient.

## Slide 17: Auto-PEEP (Intrinsic PEEP)
Definition:
Positive pressure remaining in alveoli at end-expiration due to incomplete emptying
Causes:
  Airway obstruction (asthma, COPD)
  High minute ventilation
  Short expiratory time
  High respiratory rate
Detection:
  Expiratory flow doesn't return to zero
  End-expiratory port occlusion shows pressure
  Need to trigger against positive pressure
Management:
  Increase expiratory time (decrease rate or inspiratory time)
  Bronchodilators
  Reduce minute ventilation (if appropriate)
  Apply extrinsic PEEP (80% of auto-PEEP)
Notes: Auto-PEEP increases work of breathing and can cause hemodynamic compromise. It's common in obstructive diseases.

## Slide 18: Weaning from Mechanical Ventilation
Daily Spontaneous Awakening and Breathing Trials
Readiness Criteria:
  Resolution of acute illness
  Hemodynamic stability (minimal or no vasopressors)
  Oxygenation: PaO2/FIO2 >150-200, PEEP ≤5-8
  Cough and airway reflexes present
  No pending procedures requiring sedation
Spontaneous Breathing Trial (SBT):
  CPAP 5 cmH2O, or
  T-piece, or
  Low pressure support (5-8 cmH2O)
  Duration: 30-120 minutes
SBT Success Criteria:
  RR <35
  SpO2 >90%
  HR <140 or <20% increase
  No hemodynamic instability
  No respiratory distress
Notes: Daily SBTs identify patients ready for extubation. Most patients who fail do so within the first few minutes.

## Slide 19: Weaning Parameters
Objective Measures
Rapid Shallow Breathing Index (RSBI):
  RR / VT (in liters)
  <105: Likely to succeed
  >105: Likely to fail
Negative Inspiratory Force (NIF):
  <-20 to -30 cmH2O
  Measures inspiratory muscle strength
Other Parameters:
  Spontaneous VT >5 ml/kg
  Vital capacity >10-15 ml/kg
  Minute ventilation <10 L/min
  Maximum voluntary ventilation >2× resting VE
Note: These predict success better than failure. Clinical assessment is most important.
Notes: Weaning parameters help predict success but should not replace clinical judgment.

## Slide 20: Extubation
Procedure and Considerations
Pre-Extubation:
  Suction ETT and oropharynx
  Suction below vocal cords if possible
  Position patient upright
  Explain procedure to patient
  Have reintubation equipment ready
Procedure:
  1. Deflate cuff
  2. Give positive pressure breath
  3. Remove tube at peak inspiration
4. Apply oxygen (mask or nasal cannula)
5. Encourage cough
Post-Extubation:
  Monitor closely for stridor
  Humidified oxygen
  Consider noninvasive ventilation if high-risk
  Monitor for respiratory fatigue
Notes: Proper preparation and technique reduce extubation failure. Monitor closely for signs of upper airway obstruction.

## Slide 21: Post-Extubation Management
Preventing Reintubation
Risk Factors for Extubation Failure:
  Prolonged intubation
  Weak cough
  Excess secretions
  Upper airway edema
  CHF
  Neuromuscular disease
Preventive Strategies:
  Noninvasive ventilation (prophylactic in high-risk)
  Aggressive pulmonary toilet
  Humidification
  Early mobilization
  Treat underlying causes
Reintubation Criteria:
  Respiratory failure
  Inability to protect airway
  Severe stridor not responding to treatment
  Hemodynamic instability
Notes: Prophylactic NIV may prevent reintubation in high-risk patients. Early intervention is key.

## Slide 22: Case Study 1
Patient: Mr. Smith, 65-year-old male
  Post-operative day 2 after abdominal surgery
  Intubated for respiratory failure
  Current settings: VC-AC, VT 500, Rate 14, FIO2 40%, PEEP 5
Current Status:
  Peak pressure: 35 cmH2O
  Plateau pressure: 28 cmH2O
  SpO2: 94%
  Patient appears uncomfortable, asynchronous with ventilator
Questions:
  1. Are these pressures acceptable?
  2. What might be causing the asynchrony?
  3. What adjustments would you make?
Notes: This patient shows signs of patient-ventilator asynchrony post-surgery.

## Slide 23: Case Study 1 Discussion
Pressure Assessment:
  Plateau 28: Acceptable (<30)
  Peak-plateau difference: 7 cmH2O (normal airway resistance)
  Pressures are acceptable
Asynchrony Causes:
  Pain/anxiety post-surgery
  Inadequate sedation
  Flow asynchrony (set flow may not match demand)
  Possible inadequate tidal volume for patient
Interventions:
  1. Assess pain and sedation needs
  2. Consider pressure support or PC mode for comfort
  3. Check for auto-PEEP
4. If flow asynchrony suspected, increase flow or switch to PC
5. Consider spontaneous breathing trial if criteria met
Notes: Addressing pain, sedation, and ventilator settings can improve comfort and synchrony.

## Slide 24: Case Study 2
Patient: Mrs. Johnson, 58-year-old female
  ARDS secondary to sepsis
  Day 5 of mechanical ventilation
  Current settings: VC-AC, VT 400 (6 ml/kg), Rate 22, FIO2 70%, PEEP 12
Current Status:
  Plateau pressure: 32 cmH2O
  SpO2: 88%
  Chest X-ray: Bilateral infiltrates
Questions:
  1. What is the immediate concern?
  2. How would you adjust the ventilator?
  3. What other interventions should be considered?
Notes: This patient with ARDS has high plateau pressure and hypoxemia despite high support.

## Slide 25: Case Study 2 Discussion
Immediate Concern:
  Plateau pressure 32 exceeds safe limit (<30)
  Risk of ventilator-induced lung injury
  Severe hypoxemia despite high support
Ventilator Adjustments:
  1. Decrease VT to 300-350 ml (4-5 ml/kg)
  2. Check and document driving pressure (Pplat - PEEP)
  3. Increase PEEP per ARDSNet table
4. Titrate FIO2 to maintain SpO2 88-95%
Other Interventions:
  Prone positioning if PaO2/FIO2 <150
  Consider neuromuscular blockade if severe
  Evaluate for ECMO if refractory
  Treat underlying sepsis
  Conservative fluid management
Notes: In ARDS, lung-protective ventilation is essential. Consider adjunctive therapies for refractory hypoxemia.

## Slide 26: Key Takeaways
  1. Select Mode Based on Patient Needs
  Volume control for guaranteed ventilation
  Pressure control for comfort
  Pressure support for weaning
  2. Always Use Lung-Protective Strategy
  6 ml/kg IBW, Pplat <30
  Accept permissive hypercapnia if needed
  3. Graphics Tell the Story
  Learn to recognize normal and abnormal patterns
  Waveforms guide troubleshooting
4. Treat the Patient, Not the Numbers
  Clinical assessment trumps parameters
  Comfort and synchrony matter
5. Wean Early and Daily
  Daily SBTs for eligible patients
  Use spontaneous awakening trials
Notes: Mechanical ventilation requires balancing multiple factors. Always prioritize lung protection and patient comfort.

## Slide 27: References
  1. ARDSNet. Ventilation with lower tidal volumes as compared with traditional tidal volumes for acute lung injury and the acute respiratory distress syndrome. N Engl J Med. 2000;342(18):1301-1308.
  2. AARC Clinical Practice Guidelines: Mechanical Ventilation of Mechanically Ventilated Patients. Respir Care. 2022.
  3. Girard TD, et al. Efficacy and safety of a paired sedation and ventilator weaning protocol for mechanically ventilated patients in intensive care. Lancet. 2008;371(9607):126-134.
4. Papazian L, et al. Formal guidelines: management of acute respiratory distress syndrome. Ann Intensive Care. 2019;9(1):69.
5. Tobin MJ. Principles and Practice of Mechanical Ventilation. 4th ed. McGraw-Hill; 2018.
Notes: The ARDSNet trial established lung-protective ventilation as the standard of care.

## Slide 28: Thank You
Respiratory Care Department
Excellence in Mechanical Ventilation Support