## Slide 1
Mechanical Ventilation Basics
Introduction to Ventilator Management
Presenter: [Name], RRT
Date: [Date]
Department: Respiratory Care

## Slide 2
Learning Objectives
By the end of this session, participants will be able to:
• Identify the components of a mechanical ventilator circuit
• Describe the difference between volume and pressure control ventilation
• Calculate initial ventilator settings using lung-protective strategies
• Recognize common ventilator alarms and appropriate responses
• Interpret basic ventilator graphics
Notes: These foundational skills are essential for ventilator management.

## Slide 3
Indications for Mechanical Ventilation
Primary Indications:
• **Apnea** or impending respiratory arrest
• **Acute respiratory failure**
  ○ - Hypoxemic (PaO2 < 60 on high FIO2)
  ○ - Hypercapnic (pH < 7.30 with elevated PaCO2)
• **Airway protection**
  ○ - Altered mental status
  ○ - Inability to protect airway
• **Prophylactic**
  ○ - Post-operative support
  ○ - Severe metabolic acidosis
Notes: Understanding indications helps determine when ventilation is truly needed.

## Slide 4
Ventilator Classification: By Control Variable
Type | Control | Advantage
Volume Control | Delivers set tidal volume | Guaranteed minute ventilation
Pressure Control | Delivers set pressure | Pressure limiting, variable flow
Notes: Each mode has advantages. Choose based on patient needs.

## Slide 5
Ventilator Classification: By Breath Delivery
Continuous Mandatory Ventilation (CMV)
• All breaths machine-triggered
• Patient cannot trigger additional breaths
Assist/Control (A/C)
• All breaths delivered
• Patient can trigger additional breaths
• Most common initial mode
Synchronized Intermittent Mandatory Ventilation (SIMV)
• Set rate + spontaneous breaths
• Spontaneous breaths may have pressure support
Spontaneous Modes
• CPAP: Continuous positive airway pressure
• Pressure Support: Assists spontaneous breaths
Notes: Mode selection depends on the patient's respiratory drive and condition.

## Slide 6
Lung-Protective Ventilation: ARDSNet Protocol
Tidal Volume:
• **6 ml/kg ideal body weight** (range 4-8)
• Calculate IBW:
  ○ - Men: 50 + (2.3 × inches over 5 feet)
  ○ - Women: 45.5 + (2.3 × inches over 5 feet)
Plateau Pressure:
• **Goal: < 30 cmH2O**
• If >30: decrease VT to 5 or 4 ml/kg
PEEP:
• Start at **5 cmH2O**
• Titrate based on oxygenation and hemodynamics
Notes: Lung-protective ventilation reduces ventilator-induced lung injury.

## Slide 7
Initial Ventilator Settings: Standard Starting Point
Parameter | Setting | Rationale
Mode | Volume A/C | Reliable minute ventilation
VT | 6-8 ml/kg IBW | Lung protection
Rate | 12-16/min | Normal physiologic range
FIO2 | 100% → titrate | Start high, wean quickly
PEEP | 5 cmH2O | Maintain FRC
Flow | 60 L/min | Adequate for most adults
Notes: These are starting points. Adjust based on patient response.

## Slide 8
Ventilator Graphics: Pressure-Time Waveform
Key Measurements:
• **Peak Pressure** - Total resistance + compliance
• **Plateau Pressure** - Static compliance only
• **PEEP** - Baseline pressure
Key Calculations:
**Static Compliance** = VT / (Pplat - PEEP)
• Normal: 50-100 mL/cmH2O
**Airway Resistance** = (Ppeak - Pplat) / Flow
• Normal: < 10 cmH2O/L/sec
Example:
• VT = 500 mL, Pplat = 25, PEEP = 5
• Compliance = 500 / (25 - 5) = 25 mL/cmH2O (low)
Notes: Understanding waveforms helps identify patient-ventilator problems.

## Slide 9
Common Ventilator Alarms: High Pressure
Causes:
• Secretions in airway
• Kinked ETT or circuit
• Bronchospasm
• Decreased lung compliance
• Patient-ventilator asynchrony
Response:
1. Check patient first
2. Suction if indicated
3. Check circuit for kinks
4. Auscultate for bronchospasm
5. Consider sedation if fighting ventilator
Prevention:
• Regular airway suctioning
• Proper circuit positioning
• Adequate sedation
Notes: High pressure alarms always require immediate attention.

## Slide 10
Common Ventilator Alarms: Low Pressure/Volume
Low Pressure/Volume Alarm Causes:
• Circuit disconnect
• Cuff leak
• Patient self-extubation
Response:
1. Check patient immediately
2. Verify ETT position
3. Check cuff pressure
4. Check all connections
Low PEEP/CPAP Alarm Causes:
• Large leak in system
• Circuit disconnect
• Inadequate flow
**Remember:** Low pressure alarms may indicate a life-threatening disconnect.
Notes: Low pressure alarms can indicate a catastrophic circuit disconnect.

## Slide 11
Patient-Ventilator Asynchrony: Types and Solutions
Type | Description | Solution
Trigger | Difficulty initiating breath | Adjust sensitivity
Flow | Demand exceeds set flow | Increase flow or switch to pressure control
Cycle | Premature or delayed termination | Adjust cycling criteria
Notes: Asynchrony increases work of breathing and patient discomfort.

## Slide 12
Assessment of Asynchrony
Signs of Asynchrony:
• Observe patient breathing pattern
• Check flow and pressure waveforms
• Assess for double-triggering
• Evaluate for auto-PEEP
Double-Triggering:
• Two breaths delivered back-to-back
• Indicates insufficient tidal volume
• May need to increase VT or switch to pressure control
Auto-PEEP:
• Intrinsic PEEP from incomplete exhalation
• Common in COPD and asthma
• Increase expiratory time
• Decrease respiratory rate
Notes: Addressing asynchrony improves patient comfort and ventilation efficiency.

## Slide 13
Weaning Parameters: Readiness Assessment
Spontaneous Breathing Trial (SBT) Criteria:
RSBI (Rapid Shallow Breathing Index)
• RR / VT (in liters)
• < 105 = likely to succeed
Negative Inspiratory Force (NIF)
• < -20 to -30 cmH2O
Other Parameters:
• Spontaneous VT > 5 ml/kg
• VC > 10-15 ml/kg
• Minute ventilation < 10 L/min
Clinical Assessment:
• Hemodynamic stability
• Adequate oxygenation
• Resolution of underlying condition
Notes: Weaning readiness requires both physiological and clinical assessment.

## Slide 14
Case Study: Patient Profile
**Mr. Johnson**, 70-year-old male
**Diagnosis:** Severe pneumonia, ARDS
**Height:** 5'10" (70 inches)
**Actual weight:** 90 kg
Calculate Initial Settings:
Step 1: Calculate IBW
• IBW = 50 + (2.3 × 10) = **73 kg**
Step 2: Calculate VT
• 6 ml/kg × 73 kg = **438 ml** (round to 440 ml)
Step 3: Initial Settings
• Mode: Volume A/C
• VT: 440 ml
• Rate: 14
• FIO2: 100%
• PEEP: 5
Notes: Always use ideal body weight for tidal volume calculations in ARDS.

## Slide 15
Case Study: Discussion
Questions:
1. Why use IBW instead of actual weight?
- Lung compliance, not body size, determines safe VT
2. What if plateau pressure is 35 cmH2O?
- If Pplat >30, decrease VT to 4-5 ml/kg
- May need to increase rate to maintain minute ventilation
3. When should you start weaning FIO2?
- Wean FIO2 to maintain SpO2 88-95% (ARDS)
- Avoid hyperoxia
4. What PEEP/FIO2 table might you use?
- ARDSNet PEEP/FIO2 tables guide PEEP titration
- Higher PEEP may improve oxygenation but affect hemodynamics
Notes: Lung-protective ventilation is essential in ARDS to prevent further lung injury.

## Slide 16
Key Takeaways
1. Always use lung-protective ventilation
• 6 ml/kg IBW, Pplat < 30
2. Know your calculations
• IBW, compliance, RSBI
3. Patient first, then equipment
• Always assess patient when alarms sound
4. Monitor for asynchrony
• Adjust settings to optimize comfort
5. Have a weaning plan
• Daily SBT when ready
Notes: These principles form the foundation of safe mechanical ventilation.

## Slide 17
References
1. ARDSNet. Ventilation with lower tidal volumes as compared with traditional tidal volumes for acute lung injury and the acute respiratory distress syndrome. N Engl J Med. 2000;342(18):1301-1308.
2. AARC Clinical Practice Guidelines: Mechanical Ventilation of Mechanically Ventilated Patients. Respir Care. 2022.
3. Tobin MJ. Principles and Practice of Mechanical Ventilation. 4th ed. McGraw-Hill; 2018.
4. Pilbeam SP, Cairo JM. Mechanical Ventilation: Physiological and Clinical Applications. 7th ed. Elsevier; 2020.

## Slide 18
Thank You
Excellence in Patient Care Through Education
Respiratory Care Department